## Slide 1: Advanced Design System
Design and Modelling Tool for Electronic Systems

## Slide 2: Brief History
1999
2003
2005
2011
2015
Dates based on Introduction to Author and not exact
Released and version successor to MDS
Basic Simulators- S-parameter, DC, AC, Transient, HB, Envelope, Ptolemy, MOMENTUM
Connectivity to other products
2013
IPDK
Thermal
SI

## Slide 3: Overview-Schematic
Schematic based entry
Part Selector to the left
Wire, Buses and Ground
Variable, Pin and Name Node
Probe for Current Capture
Name Node for Voltage Capture
Terminations & Excitation Sources
1
2
3
4
6
Equation Based Modelling
Simulation Controllers
5
7
8

## Slide 4: Overview-Schematic
Optimization and Design Of Experiments (DOE)
9
Data Adaptors/ Sockets
10
Design Guides
11
Dynamic Link to other software
12

## Slide 5: Overview-Layout
2D Layout Entry Tool for Planar Circuits
1
Interface to PDK, GPDK and IGPDK
2
Part Selector to the left
3
Primitives
4
Geometric Manipulations
5
Snap Options
6
Shape Manipulations
7
Fully Customizable Substrate
8
Logical Operations on Shapes
9

## Slide 6: Overview-Layout
Import from and Export to major file formats
10
Schematic Awareness (connectivity)
11
Electrical Connectivity for detecting Opens and Shorts
12
3D Visualization
13

## Slide 7: Overview-Data Display
1
Provides Display Template for Data
2
Interface to Default Dataset and many more
3
Part Selector to the left
4
Equations and Functions for Data Manipulation
5
Markers for reading Data
6
Instrument Server for writing data to a file

## Slide 8: Overview-Simulators
Bias condition for active
DC operating points
Stability of Small Signal Circuits
Frequency Response
Reflection and Transmission Characteristics of Matched stage
Frequency domain simulation of Non-Linear Circuits
Mixed domain simulation of circuits with modulated signals
Time domain simulation of circuits
Thermal Simulation of Power ICs
X-parameter modelling of Non-linear circuits
Simulation Controllers
1
2
3
4
5
6
7
8
MOMENTUM and FEM Simulators
9
Ptolemy Simulations- Data Flow
10

## Slide 9: Overview-Post Layout
Other Tools…

## Slide 10: Application Areas
Communication Systems
From System Simulation to Circuit design, modelling and simulation
System Simulation in Ptolemy (Digital Baseband), RF simulation for Transceivers and Radio Front-ends, Circuits like- ADC-DAC, IQ Modulators and Demodulators, FIR and IIR Filters, Mixers, Variable Gain Amplifiers, PLL Sub-circuits, Passives, Power Amplifiers, Low Noise Amplifiers, Microwave Filters, Antenna and sub-system
RADAR Systems and Sub-circuits
Analog Integrated Circuits
Single ended and differential gain stages, OpAmps and OTAs, Comparators, Schmitt Triger, Precision Voltage and Current References, Voltage Regulators, Protection Circuits, Switched Capacitor Circuits, Sigma Delta Modulators, Filters etc.
Digital Circuits
Logic Gates, Combinational and Sequential Circuits, Finite State Machines, Arithmetic Circuits, Microprocessor Circuits- Data Path and Control Path, Memory Controllers, SRAM and DRAM, Frequency Prescalar, MASH 1-1-1 Sigma Delta Modulator
Power Electronics Systems and Circuits
DC-DC Converters, Power Factor Correction Circuits, Power Detectors, Inverters, Motor Drives

## Slide 11: Application Areas
Control Systems and Circuits
Motion Controllers- PID, Feedback and Feed Forward Circuits, Position/ Velocity/ Torque and Power Control Loops- Analysis Design and Modelling of Control Systems
Signals and Systems
CT and DT systems, DT approximation of CT systems, Sampling, Quantization, FIR and IIR Filters, Multi-rate circuits
Electromagnetics
Transmission Lines and Waveguides, H and E Tees, Magic Tee, Waveguide Mixers, Dielectric and Cavity Resonators, Passives- Power Dividers, Hybrids, BALUN, Directional Couplers, Circulators, Transformers, Microwave Filters, Antennas and Arrays, Microwave Lenses
Cellular Planning
Channel Modelling, Cellular Planning and Layout, Analysis of Frequency Re-use and Hand-offs

## Slide 12: Third Party Technology Interface
PCB export to various file formats acceptable to manufacturers
Process Design Kits for various Semiconductor and LTCC Processes that support LVS, DRC and Tape-outs. PDKs also support thermal analysis
Third Party Libraries for SMDs and Packaged Components from various manufacturers. Modelithics supports these libraries for ADS
VHDL interface and HDL outputs for co-simulation and synthesis

## Slide 13: ADS Terminology
ADS project is called ‘Workspace’
All the resources and designs are contained in workspace folder named with _wrk extension
Design is known as Cell
Cell has three views
  Schematic
  Layout
  Symbol
Cell should have minimum one view
Cells, Notes, Data Display, Substrates are listed in Workspace tree
Every workspace has a local library
Workspace can refer to external library

## Slide 14: ADS Terminology
Designs, Data Displays and Substrates can be moved into folders in workspace tree
Sub-circuits with pins as termination can have symbol view. Schematic + symbol makes a component that can be used in bigger designs
Cells can be parametrized using Design Parameters
EM Simulated Passives can be turned into look-alike components for Circuit-EM co-simulation
Simulation results are stored in Dataset files.
Every design has dataset file with same name but can have more datasets.

## Slide 15: Typical Design/ Simulation Flow
Name should start with an alphabet. Only alphabet, numbers and underscore are valid characters.
Attach a PDK library
Set layout resolution
Default view can be schematic or layout
Use components from the palettes, wire, ground, excitation sources, DC supply and controller to make a design. Additionally, you may use pin terminations and make a component with a symbol.
START
Create a workspace
Create a cell
Perform Simulation/ Tuning/ Optimization
Are there errors, warnings, conversion issues
Solve the issues
yes
Visualize results in Data Display
STOP
no

## Slide 16: Example 1: Getting Started
We will learn to
Create a workspace
Create schematic
Perform Simulation
Visualize Data
Tune Components

## Slide 17: Creating a Workspace
Launch ADS
1
Create a New Workspace
2
Name the New Workspace
3
Use Library name same as workspace name
Setup resolution immediately
4

## Slide 18: Creating a Workspace
Use Change Libraries… button to refer to a PDK or other workspace
5
Check from listed PDKs or Add a favourite PDK
6
Choose the layout resolution
7

## Slide 19: Create a Schematic
Create a New Cell with Schematic View
1
Simulate-able design has circuit with ground and supply, terminations and excitations and simulation controller
Create the design as shown in figure
2
Hit Simulate Button
3
Plot S21 in dB on Rectangular Plot
4

## Slide 20: Tune and History
Use Tune to add tuners for inductors and capacitors
5
Enable History-On for the graph so that you can view the trend
6
History is just a visual aid, does not store component values
7
Store can be used to store tune state and Recall to restore a saved state
8
Use Update Schematic to update latest tuned values

## Slide 21: Exercise 2: DC Simulations
In this exercise, we will learn
How to attach a third party PDK
How to use Models
How to perform DC Simulation
How to sweep variables
How to change Datasets

## Slide 22: Overview of Problem
Goal: to study output and transfer characteristics of an NMOS device
Governing Equations
Output Characteristics of MOSFET
Transfer Characteristics of MOSFET
Weak

## Slide 23: Setup Workspace and PDK
Create a New Workspace
1
Add reference to PDK
2
Add reference to PDK
3
Set the layout resolution
4

## Slide 24: Organizing Workspace and Setup
Move Library Files to a Folder
5
Create a Simulate-able design as shown
6
Devices-MOS
Source- Frequency Domain
Simulation- DC
Workspace Tree
Perform Vds sweep in DC controller and Vgs sweep in Parameter Sweep referring to inner sweep in DC1 controller
10
Declare used variables using Var
7
Place Silterra Include File from Workspace Tree using Drag and Drop
9
8
Use Current Probe to measure drain current

## Slide 25: DC Simulation
Hit simulate button
11
Plot Ids in Rectangular Graph
12
Swap Vgs and Vds in controllers
13
Change Dataset for next simulation
14

## Slide 26: Plotting the Results
When simulation is complete, say no to change default Dataset. Plot Drain current from new Dataset
15
Place two markers on both the graphs on same trace
16

## Slide 27: Post Processing using equations
Use equations to write equation for rds and gm
17
Tabulate the calculated values in a table
18

## Slide 28: Exercise 3: AC Simulations
In this exercise, we will learn
How to design and simulate Analog Gain Stages
How to Perform AC Simulation
How to Plot Frequency Response
Determine Stability of Gain Stage

## Slide 29: AC Simulation
Goal: to study frequency response of various gain stages and determine their stability
AC simulation is performed on active devices to determine their frequency response and predict their stability. Prior to AC simulation active devices have to biased by performing DC Analysis. Common Single Ended Amplifiers with Current Mirror Loads are shown in figure.
Common Source
Common Gate
Common Drain

## Slide 30: Common Source Amplifier
Create Common Source Amplifier as shown in figure and perform DC Simulation
1
UGB
PM
BW
Set the AC Source with bias and perform AC Simulation
2

## Slide 31: Exercise 4:Transient Simulations
In this exercise, we will learn
To design Logic Gates
To make component with symbol
To perform Transient Simulation
To determine dynamic characteristics of CMOS Inverter

## Slide 32: Transient Simulation
Goal: to study dynamic characteristics of CMOS Inverter
Transient Simulation is time domain simulation that can be used to analyse linear as well as non-linear circuits.
CMOS Inverter
Electron Mobility is 2.5 times the hole mobility. Hence to have same source and sink currents, PMOS should be 2 and ½ times NMOS

## Slide 33: CMOS Inverter
Create CMOS Inverter as shown in figure
1
Use pin instead of terminations, DC supply and ground
2
Save and close the design. Right Click on Cell name in workspace tree to make a new symbol for the design
3
Accept the default symbol design as is and modify symbol as you wish.
4
Sub-circuit with Pins and a symbol is a component that can be inserted in bigger design by dragging and dropping into another schematic from Workspace Window
5

## Slide 34: Inverter Test Bench
Create a Test Bench to test the inverter as shown in figure
6
Perform Transient Simulation
7
Plot input and output waveforms as shown in figure
8
Use Markers, turn on Delta Mode by selecting two markers with m1 as reference.
9
Rise Time

## Slide 35: Exercise 5: S-parameter Simulations
In this exercise, we will learn
To design an Elliptic Low Pass Filter using Insertion Loss Method
To perform S-parameter simulation
To determine Return Loss, Insertion Loss and Group Delay of the filter

## Slide 36: S-parameters
Goal: to design and simulate the response of an Elliptic Filter
S-Parameter refers to reflection and transmission coefficients in terms of voltage provided all the ports, except those under investigation, are terminated into characteristic impedance of the network i.e. they do not reflect any power incident on them.
N-Port Network
Two Port
Network

## Slide 37: Elliptic Low Pass Filter
Elliptic Filters are equal ripple in pass band as well as stop band. This results in sharper rise in attenuation beyond corner frequency, ωc.
Power Loss Ratio and Transmission Characteristics of Elliptic Low Pass Filter
Pass band
1
0
Amax
Amin
Pass band
Ladder Structure for Elliptic Low Pass Filter
(Series Shunt-Resonant)
Ladder Structure for Elliptic Low Pass Filter
(Shunt Series-Resonant)
Figure is for odd N. For even N the terminations will not be same.

## Slide 38: Elliptic Low Pass Filter Design
Elliptic Filters do not have exact match on both the ports. For a given Stop Band Attenuation, a certain mismatch has to be acceptable. Unlike Butterworth and Tchebyshev designs, Elliptic filters do not have stop band attenuation charts but rather a set of tables for different pass band attenuation.
N |  | Amin (dB) |  |  |  |  |  |  | 
3 | 1.4493 | 13.5698 | 0.7427 | 0.7096 | 0.5412 | 0.7427 |  |  | 
 | 1.6949 | 18.8571 | 0.8333 | 0.8439 | 0.3252 | 0.8333 |  |  | 
 | 2 | 24.0012 | 0.8949 | 0.9375 | 0.207 | 0.8949 |  |  | 
 | 2.5 | 30.5161 | 0.9471 | 1.0173 | 0.1205 | 0.9471 |  |  | 
4 | 1.2 | 12.0856 | 0.3714 | 0.5664 | 1.0929 | 1.1194 | 0.9244 |  | 
 | 1.2425 | 14.1259 | 0.4282 | 0.6437 | 0.8902 | 1.1445 | 0.9289 |  | 
 | 1.2977 | 16.5343 | 0.4877 | 0.7284 | 0.7155 | 1.1728 | 0.9322 |  | 
 | 1.3962 | 20.3012 | 0.5675 | 0.8467 | 0.5261 | 1.2138 | 0.9345 |  | 
 | 1.5 | 23.7378 | 0.6282 | 0.9401 | 0.4073 | 1.2471 | 0.9352 |  | 
 | 1.709 | 29.5343 | 0.7094 | 1.0688 | 0.273 | 1.2943 | 0.9348 |  | 
 | 2 | 36.0438 | 0.7755 | 1.1765 | 0.1796 | 1.3347 | 0.9352 |  | 
5 | 1.05 | 13.8785 | 0.7081 | 0.7663 | 0.7357 | 1.1276 | 0.2014 | 4.3812 | 0.0499
 | 1.1 | 20.0291 | 0.813 | 0.9242 | 0.4934 | 1.2245 | 0.3719 | 2.135 | 0.2913
 | 1.1494 | 24.5451 | 0.8726 | 1.0084 | 0.3845 | 1.3097 | 0.4991 | 1.445 | 0.4302
 | 1.2 | 28.3031 | 0.9144 | 1.0652 | 0.3163 | 1.382 | 0.6013 | 1.0933 | 0.5297
 | 1.25 | 31.4911 | 0.9448 | 1.106 | 0.2694 | 1.4415 | 0.6829 | 0.8827 | 0.604
 | 1.2987 | 34.2484 | 0.9681 | 1.1366 | 0.2352 | 1.4904 | 0.7489 | 0.7426 | 0.6615
 | 1.4085 | 39.5947 | 1.0058 | 1.1862 | 0.1816 | 1.5771 | 0.8638 | 0.5436 | 0.7578
 | 1.6129 | 47.5698 | 1.0481 | 1.2416 | 0.1244 | 1.6843 | 1.0031 | 0.354 | 0.8692
 | 1.8182 | 54.0215 | 1.073 | 1.2741 | 0.0919 | 1.7522 | 1.0903 | 0.255 | 0.9367
 | 2 | 58.9117 | 1.0876 | 1.2932 | 0.0732 | 1.7939 | 1.1433 | 0.2004 | 0.9772
Amax=0.1 dB

## Slide 39: Elliptic Low Pass Filter Design
N |  | Amin (dB) |  |  |  |  |  |  |  |  |  | 
6 | 1.05 | 18.6757 | 0.4418 | 0.7165 | 0.9091 | 0.8314 | 0.3627 | 2.4468 | 0.8046 | 0.9986 |  | 
 | 1.1 | 26.237 | 0.5763 | 0.888 | 0.6128 | 0.973 | 0.5906 | 1.3567 | 0.9431 | 1.0138 |  | 
 | 1.158 | 32.4132 | 0.6549 | 1.0036 | 0.4597 | 1.0923 | 0.7731 | 0.9284 | 1.0406 | 1.0214 |  | 
 | 1.2503 | 39.9773 | 0.7422 | 1.1189 | 0.3313 | 1.2276 | 0.9746 | 0.626 | 1.1413 | 1.0273 |  | 
 | 1.3024 | 43.4113 | 0.7751 | 1.1631 | 0.287 | 1.2832 | 1.0565 | 0.5315 | 1.1809 | 1.0293 |  | 
 | 1.3955 | 48.9251 | 0.8289 | 1.2243 | 0.2294 | 1.3634 | 1.1739 | 0.4148 | 1.2366 | 1.0316 |  | 
 | 1.5962 | 58.4199 | 0.8821 | 1.3085 | 0.1565 | 1.4792 | 1.3421 | 0.2757 | 1.3148 | 1.0342 |  | 
 | 1.7032 | 62.7525 | 0.9115 | 1.3383 | 0.1321 | 1.5216 | 1.4036 | 0.231 | 1.3429 | 1.035 |  | 
 | 1.7927 | 66.019 | 0.9258 | 1.3583 | 0.1162 | 1.5505 | 1.4453 | 0.2022 | 1.3619 | 1.0355 |  | 
 | 1.8915 | 69.3063 | 0.9316 | 1.3765 | 0.1019 | 1.5771 | 1.4837 | 0.1767 | 1.3794 | 1.0358 |  | 
7 | 1.05 | 30.5062 | 0.9194 | 1.0766 | 0.3422 | 1.0962 | 0.4052 | 2.2085 | 0.8434 | 0.5034 | 2.2085 | 0.411
 | 1.1 | 39.3517 | 0.9882 | 1.1673 | 0.2437 | 1.2774 | 0.5972 | 1.3568 | 1.0403 | 0.6788 | 1.3568 | 0.5828
 | 1.1494 | 45.6916 | 1.0252 | 1.2157 | 0.194 | 1.5811 | 0.9939 | 0.5816 | 1.2382 | 0.5243 | 0.5816 | 0.4369
 | 1.25 | 55.4327 | 1.0683 | 1.2724 | 0.1382 | 1.7059 | 1.134 | 0.4093 | 1.4104 | 0.7127 | 0.4093 | 0.6164
 | 1.2987 | 59.2932 | 1.0818 | 1.2902 | 0.1211 | 1.7478 | 1.1805 | 0.3578 | 1.4738 | 0.7804 | 0.3578 | 0.6759
 | 1.4085 | 66.7795 | 1.1034 | 1.3189 | 0.094 | 1.8177 | 1.2583 | 0.277 | 1.5856 | 0.8983 | 0.277 | 0.7755
 | 1.5 | 72.1183 | 1.1159 | 1.3355 | 0.0786 | 1.7569 | 1.1517 | 0.3716 | 1.6383 | 1.125 | 0.3716 | 0.9559
 | 1.6129 | 77.9449 | 1.1272 | 1.3506 | 0.0647 | 1.8985 | 1.3485 | 0.1903 | 1.7235 | 1.0417 | 0.1903 | 0.8913
 | 1.6949 | 81.7567 | 1.1336 | 1.359 | 0.057 | 1.9206 | 1.3734 | 0.1675 | 1.7628 | 1.0823 | 0.1675 | 0.9231
 | 1.8182 | 86.9778 | 1.1411 | 1.369 | 0.0479 | 1.9472 | 1.4033 | 0.1408 | 1.8107 | 1.1316 | 0.1408 | 0.9616
Amax=0.1 dB

## Slide 40: Low Pass Filter Design
Filter Specifications
and desired attenuation in stop band is >30 dB
N |  | Amin (dB) |  |  |  |  |  |  | 
5 | 1.2 | 28.3031 | 0.9144 | 1.0652 | 0.3163 | 1.382 | 0.6013 | 1.0933 | 0.5297
Compute Inductors and Capacitors using given equations
1
Define Design Parameters as R0 and fc
2
Create sub-network with its symbol
3

## Slide 41: Response of Elliptic Low Pass Filter
Create a test bench as shown in figure, to test the filter response
4
Enable Group Delay in simulation controller under Parameter Tab
5
Perform Simulation and Plot the Response as shown
6

## Slide 42: Exercise 6: EM Simulations
In this exercise, we will learn to
Specify custom substrate
Layout an inductor and a capacitor on chip
Model inductor and capacitor

## Slide 43: Introduction to Substrates
ADS provides (1) MOMENTUM, a Method of Moment based 2.5 D simulator
(2) FEM, Finite Element Method 3 D simulator
Layout is a 2 D entry tool, hence z-axis information is specified as Metal Stack with sandwich dielectric. Substrate Height, Metal thickness and electrical properties have to be specified. Two metal layers are connected through conductor via. We specify 5+1 Metal Stack as shown in figure.
Cu,
Silicon Dioxide,
Silicon Nitride,
Silicon,
Material

## Slide 44: Metal Stack
UTM, Cu, 7µm
ViaT, Silicon Dioxide, 4µm
TopMetal, Cu, 2µm
Via4, Silicon Dioxide, 2µm
M4, Cu, 1µm
Via3, Silicon Nitride, 0.05µm
M3, Cu, 1µm
Via2, Silicon Dioxide, 1µm
M2, Cu, 1µm
Via1, Silicon Dioxide, 1µm
M1, Cu, 1µm
Via0, Silicon Dioxide, 1µm
M0, Cu, 0.67µm
Silicon Dioxide, 1µm
Silicon, 100µm
Cond, Cu, 1.34 mil
Right click on workspace tree and create new substrate
1
Let the template be anything
Create new drawing layers using Technology> Layer Definitions
2

## Slide 45: Substrate in ADS
Role
Layer Colour and Pattern
Add material from Database
3

## Slide 46: Substrate in ADS
Create the metal stack with thicknesses of various layers as shown in figure
4

## Slide 47: Inductor Design
Goal: to design a 2.5 nH inductor at 3.3 GHz
Inductors are spiral traces with ground as far as layout size permits. Despite this designer has to have ground continuity between two ports. For predictability termination of electric lines of flux should be fixed i.e. inductor can be surrounded with ground at sufficiently large distance.
Layout a spiral inductor on UTM layer using Transmission Line Microstrip palette. Instead of air bridge or underpass use stacked inductor on UTM to spiral in and Top Metal to spiral out.
5
Use following dimensions
L1=L2=152 µm
Trace width is 10 µm and gap is 10 µm
6

## Slide 48: EM Simulation Setup
At the two ends of the inductor place two ports followed by two ports for local grounds. All signal ports should be connected first before ground reference ports
7
Setup EM Simulation
8
Set port 3 as ground reference for port 1 and port 4 as ground reference for port 2 using Port Editor
9
Set simulation frequency as 3.3 GHz single point
10
Enable Transmission Line Mesh and Edge Mesh in Option> Mesh
11
Hit Simulate Button
12

## Slide 49: Inductor Simulation Results
Plot S11 on Smith Chart. Write the following equations to compute inductance and series resistance
13
Tabulate Inductance and Series Resistance.
14
Run the simulation from 0 Hz to 18 GHz
15

## Slide 50: Capacitor Design
Layout the MIM (Metal-Insulator-Metal) capacitor as shown in figure. M4 is the top plate of MIM and M3 is the bottom plate. M4 has inclusion rule on M3 of 1 um.
16
We wish to design 2 pf capacitor at 3.3 GHz. Dimensions of Top Plate of capacitor is 36 um x 36 um

## Slide 51: Exercise 7: EM-Circuit Co-simulations
In this exercise, we will learn to
Create a look-alike model of Inductor
Create a VCO-core and simulate its start-up characteristics

## Slide 52: Generating a Look-alike symbol
If you have made sure that EM model is generated at the time of EM simulation, you can drag and drop the inductor from Workspace Tree
1
Goal: to design a VCO operating in commercial defence band (3.1 GHz to 3.5 GHz). We wish to use the designed inductor in LC circuit

## Slide 53: Voltage Controlled Oscillator
Create a VCO with Start-up Circuit
2

## Slide 54: Simulation Response of VCO
Simulate for Vc=0 V, 0.4 V and 0.7 V
3

## Slide 55: Exercise 8: Harmonic Balance
In this exercise, we will learn to
Design a Class E High Efficiency Amplifier
Perform Harmonic Balance Simulation
Plot Harmonics
Compute Power, Gain, Power Added Efficiency

## Slide 56: Introduction to Class E Power Amplifier
Goal: to design and simulate Class E Power Amplifier and understand trade-offs
Applications
High Efficiency DC-DC Converters
High Efficiency constant envelope power amplifiers
Operation
100% Drain Efficiency by removing losses in load network
Voltage across the device and current through the device in quadrature
Switch-on of the device is smooth i.e. no power stored in load network
Class E Topology
Load Network consists of shunt capacitor and series tuned LCR circuit
Assuming Series LC are ideal, the only power dissipation is in the load
Radio Frequency Choke is the source of Direct Current
Switch Capacitor combination traps all current harmonics
Series LC traps all voltage harmonics

## Slide 57: Class E Waveforms
Compute Class E Waveforms, design and important parameters
1

## Slide 58: ADS Schematic for Class E Simulation
Setup Class E amplifier as shown in figure. Set Harmonic Balance Controller as shown. Simulate and plot Class E waveforms. Tabulate Drain Efficiency and Output Power
2

## Slide 59: Simulated Waveforms of Class E PA

## Slide 60: Exercise 9: Ptolemy Simulations
In this exercise, we will learn to
Design QPSK Source
Plot various constellations
Study the effect of VCO Phase Noise on Demodulated Signal

## Slide 61: QPSK Source
Create New Schematic with following Design Parameters
1
Goal: to design QPSK source in Ptolemy and study the effect of phase noise on demodulation

## Slide 62: QPSK Source Design
Compute inputs from Design Parameters in a variable
2
Set the data source and splitter as shown
3

## Slide 63: QPSK Source Design
Process the I and Q channels as shown in figure and input filtered IQ channels into QPSK Modulator
4

## Slide 64: QPSK Test Bench

## Slide 65: Demodulation with VCO Phase Noise

## Slide 66: Exercise 10: Envelope-Ptolemy Co-Simulations
In this exercise, we will learn to
Input modulated signal into PA model
Plot output spectrum
Compute ACPR

## Slide 67: Power Amplifier Non-linearity
Goal: To model a Non-linear Power Amplifier in Harmonic Balance and determine ACPR for QPSK Modulated Signal Input
Create New Schematic with Amplifier Model from System- Amps & Mixers Palette
1
We are using TOI and SOI to model amplifier non-linearity. TOI is 8 to 10 dB above 1 dB compression point and SOI is usually 14 dB above that. Amplifier is 1 dB compressed at 14.3 dBm input

## Slide 68: Single Tone HB Response
Sweep RF power to simulate 0.5 dB and 1 dB compression points
2

## Slide 69: PA Component for Envelope-Ptolemy Co-simulation
Create a PA Model with Envelope Controller as shown in figure. Tstop and Tstep are design parameters. You can give Tstep default value as 1 us and Tstop default value as 100 us.
3

## Slide 70: DF simulation bench
Copy the test bench from previous Ptolemy simulation and modify as in figure. The changes are marked in the figure
4

## Slide 71: Ptolemy-Envelope Co-simulation Results
Plot output spectrum for two values of input power just to study spectral re-growth (-20 dBm and 14 dBm)
5
Pin=14 dBm
Pin=-20 dBm

## Slide 72: Smith Chart and Matching
Matching Techniques

## Slide 73: S-Parameters
Scattering parameters are indirectly established through power measurements. Scattering Parameters or S-parameters in short are reflection and transmission coefficients under a special condition that all ports other than those under investigation are not the source of power into the network. This is true when all other ports are matched in characteristic impedance of the network. In case all the other ports are matched for maximum power out i.e. to port conjugate impedance, S-parameters are known as Generalized S-Parameters.
Where represents peak amplitude of incident wave and represents peak amplitude of reflected wave at input port. Similarly
Two Port
Network

## Slide 74: N-port Network
N-Port Network
Let there be two ports under consideration 1 and n. All other ports are terminated in characteristic impedance of the network. Let be the power of incident wave at port x, be the power of reflected wave at port x and be the power out at port n due to power incident at port x. Thus S-parameters are defined as

## Slide 75: Characteristic Impedance
2 Port Network
1
1’
2
2’
Max. Power Transfer Plane
Max. Power Transfer Plane
1
1’
2
2’
Max. Power Transfer Plane
Max. Power Transfer Plane
Characteristic Impedance is a special case of Driving Point Impedance. In 2-port network with two terminations as and such that impedance looking into the network at port 1 is complex conjugate and impedance looking into the network at port 2 is complex conjugate . This assures maximum power transfer at both the ports. and are called Driving Point Impedances. In case , is Characteristic Impedance.

## Slide 76: Free Space Wave
In lossless charge free medium, electromagnetic waves travel supporting each other as predicted by Maxwell’s Curl Equations
The solution is
Loss Tangent
Propagation Constant
Attenuation Constant
Phase Constant
Characteristic Impedance
Phase Velocity
Wavelength

## Slide 77: Guided Wave (TEM)
(a)
(b)

## Slide 78: Propagation Constant (TEM Guided Wave)
Attenuation Constant
Phase Constant
Corner Frequency
Phase Velocity
Wavelength

## Slide 79: Characteristic Impedance (TEM Guided Wave)

## Slide 80: Travelling Wave Vs. Discontinuity
Source
Interface
Z
V
Standing wave pattern
Travelling wave
At the interface z=0 gives
Normalized Impedance
Normalized Impedance
,
and

## Slide 81: Line Terminated in any Impedance
Impedance at any point before z=0 for lossless line is given by
Let be the length from the load
Standing Wave Periodicity
For

## Slide 82: Introduction to Smith Chart
Centre of the Smith Chart represents where is characteristic impedance of the system or the line. At the center, and
The edge of the Smith represents and . Two points on this circle are for and for
where reflection is due to load

## Slide 83: Reactance Circles
These circles are centered on vertical line at and . Radius of circles is . Hence all the circles pass through 1,0. In case , all the circle centers are on positive . In case , all the circles are on negative . A series C=0 represents a circle at 1,0 with radius as 0. A series L=∞ represents a circle at 1,0 with radius as 0. Both cases are open circuit. Figure shows the reactance circles.

## Slide 84: Impedance Chart
Series R
Series R
Increasing Series L
Decreasing Series C
Constant VSWR
A series transmission line with same characteristic impedance as the center of the Smith Chart moves the impedance on concentric constant VSWR circles. A series Transmission Line of Higher Impedance than the center will move the impedance towards Open and of Lower Impedance than the center will move the impedance towards Short.

## Slide 85: Quarter Wavelength Line
Normalized Impedance is inverted by Quarter Wavelength Line
can be matched to by quarter wavelength long line between the two
Shunt G
Shunt G
Decreasing Shunt L
Increasing Shunt C
Shunt Elements can be matched using Admittance Chart.
For Short Circuited Stub
For Short Circuited Stub

## Slide 86: Exercise 11: Impedance Matching
In this exercise, we will learn to
Match arbitrary impedance to 50 Ω
Broadband Match
We will use Transmission Lines and Lumped Components to do the matching

## Slide 87: Quarter Wave Transformer
Goal: design Quarter Wave Transformer to match 3 Ω to 50 Ω
3Ω
6Ω
12Ω
25Ω
50Ω
We will match 3Ω to 6Ω to 12Ω to 25Ω to 50Ω using quarter wavelength lines between two impedances. Design Frequency is 9.5 GHz.
Create New Schematic with Quarter Wave Transformer
1
Perform S-Parameter Simulations
2
Plot S-Parameters
3

## Slide 88: Line Calc for Transmission Line Design
Goal: design Microstrip Line of desired impedance using Line Calc
Let us use FR4 substrate with 10 mil height. First section is 4.2Ω.
4
Repeat the procedure for 8.5Ω, 17.3Ω, and 35.35Ω
5

## Slide 89: Quarter Wave Transformer using µ-strip line
Characteristic Impedance | µ-strip Width in mil | µ-strip Length in mil
4.2Ω | 401 | 148.5
8.5Ω | 185.2 | 151.5
17.3Ω | 80.4 | 156.8
35.35Ω | 30.77 | 165.25
Ideal
µ strip
Create Quarter Wave Transformer using µ-strip lines and simulate
6

## Slide 90: Auto Layout Generation
Create a new schematic and copy paste the transformer as shown
7
Auto generate layout
8
Define substrate, add ground plane, add ports (port 1 is 3Ω and port 2 is 50Ω) and perform EM simulation
9

## Slide 91: EM Simulation of Q-Wave Transformer
EM
circuit
EM
circuit

## Slide 92: Low Pass Match
Goal: Match 4+j8 to 50Ω using single pole matching at 9.5 GHz
8.5 GHz
10 GHz
8 GHz
13 GHz
The Issue…

## Slide 93: High Pass Match
The Issue…
8.5 GHz
10 GHz
8 GHz
13 GHz

## Slide 94: Two Pole Band Pass Match
Same match can be designed using Low Pass- High Pass poles
Series L
Shunt C
Series C
Shunt L
The Issue…
Precise non-standard component values

## Slide 95: Ferro A6S All Silver Green Tape
LTCC Process Description and ADS setup

## Slide 96: Green Tape
FERRO
Ferro Green Tapes are low cost patented Calcium Borosilicate tapes available in two thicknesses – 10 mil (254 µm) and 5 mil (127 µm). For our applications we will use 5 mil tapes. Non-standard thicknesses are 60 µm and 100 µm. These dimensions are pre-Co-firing.
Shrinkage upon Co-firing | 
XY | 15.3%±0.2%
Z (un-laminated to fired) | 24%±0.2%
Metallization is Self-Adhering Metallization (SAMS). Metallization is of following types
All Silver Based
All Gold Based
Mixed Metal System
We will use ASB with normalized fired metal thickness of 6 to 9 µm (post firing)
1 10 20 30 40 50 60 70 80 90 100
8
7
6
5
4
3
2
0.0105
0.0085
0.0075
0.0065
0.0055
0.0045
0.0035
0.0025
0.0015
0.0005
0.000
Dielectric Constant
Loss Tangent
Frequency (GHz)

## Slide 97: Typical LTCC Stack
Cavity
Buried Thick film Resistor
Surface Thick film Resistor
Thermal Via
Buried Interdigited Capacitor
Blind Via
Buried Stacked Via
Staggered Via
Pin
Pad
Window Frame / Heat Sink
Post Fired Processing

## Slide 98: LTCC Processing Steps
Step 1: Unreeling the tape
Comes with polyester backing, to be retained till lamination, no pre-conditioning required (may distort the tape)
Step 2: Blanking
Ferro LTCC Tapes can be blanked by hot knife, die cutting or lasering. Blanking refers to cutting tapes to standard, preferably square, shape and size. Green tape is lead free and non toxic making disposal of scrapes easy.
Step 3: Frame and Register
Registration holes are punched into tapes during blanking or subsequently. Tapes can be mounted on to frames using rubber adhesives. Cross plying of alternate layers is not required.
Step 4: Punch Vias and Cavities
Registration holes are punched into tapes during blanking or subsequently. Tapes can be mounted on to frames using rubber adhesives. Cross plying of alternate layers is not required.
Step 5: Conductor Printing
Metal compounds with matching shrinkage are used to screen print conductors
Step 6: Registration and Lamination
Registration is the process of stacking green tape layers using metal cast. Lamination is treating under pressure the layers so that they stick together
Step 7: Co-firing
To avoid buckling, uniform metal loading on exposed layers, stress relaxation using holes and cut-outs, flipping during firing

## Slide 99: Post Co-firing Processing
Post Co-firing a two-paste process can be used to create landing features for window frames, pins and heat sinks. Temperature coefficient of Expansion of metal alloy has to be matched to that of fired ceramic. Dicing can be done mechanically or using laser.
ASB Materials and Metallization Properties
Fired Physical Properties | 
TCE (25-300 ̊ ) | <8 ppm/ ̊ C
Fired Density | 2.43 g/
Flexural Strength | >160 M Pa
Thermal Conductivity | 2W/ mK
With Thermal Vias | >50W/ mK
Fired Physical Properties | 
TCE (25-300 ̊ ) | <8 ppm/ ̊ C
Fired Density | 
Flexural Strength | >160 M Pa
Thermal Conductivity | 2W/ mK
With Thermal Vias | >50W/ mK
Fired Electrical Properties | 
Dielectric Constant (1 to 100 GHz) | 5.9±0.2
Loss Tangent (1 to 100 GHz) | <0.002
Insertion Loss (10 GHz) | <0.18 dB/inch
Bulk Resistivity | >Ω/cm
Fired Electrical Properties | 
Dielectric Constant (1 to 100 GHz) | 5.9±0.2
Loss Tangent (1 to 100 GHz) | <0.002
Insertion Loss (10 GHz) | <0.18 dB/inch
Bulk Resistivity | 

## Slide 100: All Silver Base Material (Metal)
Material Type | Material | Firing
Inner Conductor | CN 33-398 | Co-fireable
Resistor Termination | CN 33-391 | Co-fireable
Via Fill | CN 33-343 | Co-fireable
Surface Conductors |  | 
Standard | CN 33-391 | 
Pure Silver | 3309 | Post-Fireable
Solder able | 3350 | Post-Fireable
Resistor | FX 87 Series | Co-fireable
CN 33-343
Silver Via Fill Paste
Typical Properties | 
Solid Content | 88.5-91.5%
Fineness of Grind | 24/22 µm
Coverage | 60
Print Conditions | 
Brass or Stainless-Steel Stencil (1 mil to 3 mil) | 
Dry Conditions | 
15 min to 1 hr. at room temp or 10 min at 70 ̊C | 
Co-Firing flow | 
2 ̊C/min from room temperature to 450 ̊C, 2 hr. at 450 ̊C, 8 ̊C/min to 850 ̊C, 10 min at 850 ̊C | 
Resistivity | ≤2 mΩ/sq.
Typical Properties | 
Solid Content | 88.5-91.5%
Fineness of Grind | 24/22 µm
Coverage | 
Print Conditions | 
Brass or Stainless-Steel Stencil (1 mil to 3 mil) | 
Dry Conditions | 
15 min to 1 hr. at room temp or 10 min at 70 ̊C | 
Co-Firing flow | 
2 ̊C/min from room temperature to 450 ̊C, 2 hr. at 450 ̊C, 8 ̊C/min to 850 ̊C, 10 min at 850 ̊C | 
Resistivity | ≤2 mΩ/sq.
CN 33-391
Termination of resistances, Solder able Surface Metal
Typical Properties | 
Solid Content | 70%
Print Thickness | 9-12 µm (pre) 6-9 µm (post)
Resistivity | ≤1 mΩ/sq.
Solderability | >95%
Thinning is not recommended. With shelf life, evaporation of solvent can be complemented by Ferroflo Thinner 0804
Printing, Drying & Firing are as discussed with CN 33-343
Storage & Shelf Life
Should be stored in cool & Dry conditions away from sun light. Self life of more than 6 months is possible

## Slide 101: Exercise 12: Passive Designs
In this exercise, we will learn to
design and simulate planar transmission lines
model transmission lines using pi equivalent
design, simulate and model inductors and capacitor
design, simulate and model commonly used passives

## Slide 102: Layers and material in LTCC Process
Goal: to design Transmission Lines in LTCC Process
Create a workspace with millimetre as layout unit. Create 8 Layer LTCC Process Stack
1

## Slide 103: Substrate Definition for A6S ASB
We will use Vias for Thermal Vias as well though Thermal conductivity of Silver Filled Vias is 174 W/ mK while that of thermal Vias is 50 W/mK

## Slide 104: CPWG in LTCC Process
For the design we are assuming line on M7 and ground on M5.

## Slide 105: CPWG Line Layout
Layout CPWG Line as shown in figure and perform EM Simulation
2

## Slide 106: High Frequency Stacked Inductor

## Slide 107: 10 mil green tape
The only change in substrate is that the fired height of each layer is 186 µm.
Save the LTCC substrate as 10 mil substrate and change heights of all layers to 186 µm. Change the substrate for the inductor in EM setup and perform EM simulations.

## Slide 108: Dual MIM Capacitors in FERRO A6S
5 mil Green Tape

## Slide 109: Dual MIM with Interdigit edges

## Slide 110: Dual MIM Capacitor plain edges
Resonant Frequency is slightly lower
Capacitance is slightly lower
What remains to be studied is reliability

## Slide 111: Power Dividers
Goal: to design and simulate a 2 way Wilkinson Divider
Use Line Calc to determine dimensions of Quarter Wave 70.7Ω and 50Ω CPWG at 9.5 GHz on M7 with M5 as ground.
1
70.7 Ω CPWG on M7 with M5 as ground
50 Ω CPWG on M7 with M5 as ground
,
,

## Slide 112: Simplified Layout for Faster Simulation
Computation Load and Time are two major factors in development that have to be minimized. This requires design to be simplified based on symmetry and small features. Small features like numerous vias should be combined into one. Use your intuition to reduce the number of vias.
2

## Slide 113: 90֯ Hybrid
50 Ω CPWG on M7 with M5 as ground
35.35 Ω CPWG on M7 with M5 as ground

## Slide 114: Exercise 13: Filter Design Guide
In this exercise, we will learn to
Design a filter using filter design guide
Layout the filter and EM simulate its response

## Slide 115: Design Guide
Goal: to explore Filter Design Guide and put it to use to design an Elliptic Filter
Design Guides are packages that automate or assist the design of various sub-systems
Launch the Filter Design Guide
1
Place BPF component from Filter DG- All on to schematic
2

## Slide 116: Filter Design Assistant
Specify the desired filter characteristics. Check Realizations View All
3
Hit Design. Cycle through various realizations and select one among the designs
4

## Slide 117: Simulation Assistant
In Simulation Assistant tab, select the simulation frequency and hit simulate. You can hit Create Template to create a schematic for simulations later.
5

## Slide 118: Yield Assistant
A gaussian statistical variation on each component with standard deviation of 5% can be specified. Component value can be enabled for yield optimization.
6
constraints on filter specifications can be set for qualification of filter
Hit optimize to perform the yield optimization. You can optionally create a template to perform yield optimization manually at later point
7

## Slide 119: Filter Realization
At this point you have a filter for implementation. Notice that there are 7 anti-resonant circuits that have to be accurately designed. You can proceed to do so manually or perform Lumped to Distributed Transformation.
8
At this point, you can save a copy of the filter design for the manual approach. This might close the Filter Assistant but you can launch it later from the template you created.

## Slide 120: Lumped to Transmission Lines to Microstrip
Some resonant circuits offer themselves for single step transformation to Microstrip, while others may need Lumped to TL to TL (Kuroda) and then to
9
Microstrip Transformation.
Layout is critical due to distributed ground and parasitic and will be presented by the presenter at the end of the exercise
10

## Slide 121: Exercise 14: LTCC Package Design
Package Design and Simulation

## Slide 122: SMA Jack and Number of Layers
1 mm
Create the Metal Stack as shown in Figure in ADS
1

## Slide 123: Steps for LTCC Package Design
FEM out
LNA out
PA out
Vddp
Vddn
Vgp1
Vgp2
Vgp3
Vgl1
Vgl2
Vsn
Vsp
Layout the Package as shown in Figure. Note that Thermal Vias are large (0.4 mm radius) while other vias are small (0.05 mm radius)
2
Separately simulate the SMA to Microstrip Transitions before including them on to Module. These transitions are critical
3
All layers except M0 removed from under the Transition
4
CPWG Lines are
5
Wire Bonding Pads are 0.5 mm x 0.5 mm

## Slide 124: Design Simplification for EM Simulation
Simplified Layout for EM Simulation
3D EM preview of LTCC Module
6
Combine round Vias into rectangular Vias
Convert round Thermal Vias to rectangular Vias

## Slide 125: Multi-Technology Demo
7
Follow Multi-Technology Flow with the Instructor in ADS using FEM Solver
OR
7
Export the design to EMPro with the click of a button in EM simulation settings
The difference in the flow is that the chip would be the part of the Multi-Technology Flow. There is a disconnect at this step in design. The flow is good for validation after the design has been finished. A continuous design flow simulates LTCC Package separately and MMIC separately
This would open EMpro with the 3D LTCC. At this point it is advisable to make all the models editable and copy them to workspace tree. You can merge all connected metal structures and dielectric structures. You can name every Line as per the functionality they have.

## Slide 126: 3D Package with Cavity in EMpro

## Slide 127: Bond Wires
8
You can add bondwire definitions under definition tab in workspace tree
9
You can add bond wires to connect Pads on the chip to the pads on the package

## Slide 128: Material Definition and Assignment
10
You can add a material from database or define material properties for those not available in database.
11
You can assign a material to an object by drag and drop.

## Slide 129: Ports
12
You can use Waveguide Ports for those on the edges but for internal ports you have to have port definition
13
You can add a port with No Definition and later define its placement and characteristics

## Slide 130: Port Assignment
Port 1
Port 2

## Slide 131: FEM Simulations
14
Once you are done with Ports, you are ready for specifying the Bounding Box and Absorbing Boundaries. You can check the default settings
15
Set the frequency for simulation as single point (9.5 GHz). Launch the simulation and wait for the results
16
Plot the reflection and transmission coefficients for RF Lines
PA Input Line

## Slide 132: Results- LNA Output Line
LNA Output Line

## Slide 133: Results- FEM Antenna Line
FEM Antenna Line
From these simulations
You can assume LNA Noise Figure to degrade by 0.12 dB plus 0.1 dB of connector loss plus speculated IRF loss of 1 dB
Power at the antenna would be lower by same numbers
Ports capture the ground inductance effects as they are referenced to local grounds. This means that you can safely connect the EM simulated lines to the design without worrying about ground inductance. The reference of the ports can be global ground as the effects of ground inductances are captured in S Parameters
Discussion on Ground Inductance

## Slide 134: Across Band Simulation & EM Model
Package should be simulated up to 5th Harmonic which is approximately 50 GHz.
17
Once simulation is complete you can export the EM Model to ADS as shown

## Slide 135: Importing EM Model into ADS
18
Copy the package to ADS working directory.
19
Use Manage Libraries from ADS Main Window to add the library with EM Model for Ceramic Package
20
You can copy the model to project library and make a more easy to use symbol.

## Slide 136: GaN Process
UMS Process

## Slide 137: UMS GaN Process

## Slide 138: Key Rules

## Slide 139: Layout Rules

## Slide 140: Layout Rules

## Slide 141: Layout Rules

## Slide 142: Low Noise Amplifier
Operation and Specifications

## Slide 143: Role of Low Noise Amplifier
Amplifies signal with least possible contribution to Noise. In classic receiver noise analysis, thermal noise is considered as the only source of noise. Thus for a receiver
Where, NF is cascaded Noise Factor of the receive chain
Noise Factor of the receive chain is given by Friis Formula
…
Leading up to detector
All the losses between Antenna and LNA input are directly added to Noise Factor
Noise Factor of LNA contributes directly to the receiver Noise Factor. Rest of the Gain Blocks have their Noise Factor minus 1 divided by total gain prior to that Gain Block. Thus we can see that Noise Factor of LNA, and Loss of Image Reject Filter must be minimized.

## Slide 144: LNA Electrical Characteristics
Gain
Power Gain is the ratio of output power to input power and can be expressed in dB as
Power gain includes mismatch losses at input as well as output. LNA is not only matched for Maximum Gain but also for Noise Figure (Factor). Hence Available and Transducer Gains can be investigated.
Higher the Gain of LNA, lower the effect of Noise of succeeding Gain Stages on over all receiver Noise Figure.
Return Losses
Ratio of incident and reflected powers expressed in dB is called Return Loss. In case of simultaneous conjugate match at input and output, Reflection Coefficients are same as and
Noise Factor (Figure)
Ratio of Gain offered by a stage to Noise and that to Signal is known as Noise Factor. When expressed in dB, the quantity is known as Noise Figure. Ideally, Noise Factor should be 1 or Noise Figure should be 0dB.
Half IF components fall in band and cause increase of Noise Figure due to second order mixing. SOI (Second Order Intercept and Image Rejection becomes important. In low IF and direct conversion both TOI and SOI become important.

## Slide 145: LNA Electrical Characteristics
Input Second Order Intercept (SOI)
Input Power, at which the IM2 components have same magnitude as the signal magnitude provided a linear gain, is called Input SOI. In dB, IM2 Gain is twice that of Linear Gain. Thus SOI is greater than TOI.
Input Third Order Intercept (TOI)
Input Power, at which the IM3 components have same magnitude as the signal magnitude provided a linear gain, is called Input TOI. In dB, IM3 Gain is times that of Linear Gain.
Spurious Free Dynamic Range (SFDR)
Least detectable signal amidst noise is called Sensitivity. Sensitivity is a function of LNA Noise Figure, Gain, System Bandwidth and Temperature. The highest input for LNA is considered as Input TOI. Range between sensitivity and TOI is referred to as SFDR.
Stability
Stability at small signal is established using Source and Load Stability Circles. Stability can be expressed as Spurs in dBc. Stability can also be established using K (K>1 for in-band as well as out-band and for entire SFDR)

## Slide 146: Noise Sources in Active Devices
Electrical Noise in active devices is of the form of random current and voltage fluctuations. The source of these noises is mainly the discrete nature of charge or random motion of carriers or scattering from defect sites and alloy impurities. Extraneous pickup of noise will be discussed later.
Most of the devices have PN junctions that are forward or reverse biased. In reverse biased diode, the leakage current is very small. Noise becomes significant in case of forward biased diode due to accompanying current.
Noise
Shot Noise
Thermal Noise
Flicker Noise
Burst Noise

## Slide 147: Shot Noise
Na
Nd
x
Carrier Distribution across forward biased PN Junction
Minor fluctuations in the number of carriers crossing the junction causes shot noise. The current is composed of bursts of charge crossing the junction with random time intervals.
Shot Noise Power Spectral Density
f
White Noise
The minimum time for transition, , through the junction sets the upper limit on the frequency, 1/, up to which such a noise is present.
Reverse Biased Junctions have very small leakage current and hence do not contribute to Shot Noise

## Slide 148: Thermal Noise
Unlike the Shot Noise, Thermal Noise is present in active and passive devices due to random motion of carriers in physical resistances. This random motion of carriers is directly proportional to the temperature. Shot Noise is independent of temperature.
Like Shot Noise, Thermal Noise Spectral Power Density is independent of frequency. Current or voltage fluctuations have Gaussian Probability Density Function about their mean values.
Small Signal Thermal Noise Model of a resistor
Thermal Noise Spectral Density can be specified as mean square current or voltage per unit bandwidth or root mean square current or voltage per unit bandwidth root. It can also be specified as equivalent thermal resistance.
Thermal Noise extends to much higher frequencies than Shot Noise which is limited by smallest transition time through the junction. Thus at high frequencies one can expect only thermal noise as white noise.

## Slide 149: Flicker Noise
Source of Flicker Noise is carrier traps due to crystal defects in bulk or at polycrystalline interface with the semiconductor. These traps capture & release carriers with randomly varying time intervals. Most of the time intervals are large causing most of the energy to be concentrated around low frequencies. Flicker noise is process dependent and can vary from wafer lot to wafer lot as well as device to device on same wafer. PCM (Process Control Monitor) can provide insight into on wafer variations.
where is process dependent parameter
a can vary between 0.5 to 2
b can be 1 or higher
f
log scale
log scale
For low noise avoid bulk resistors and use metal film resistors.
Larger the defect area more are the trap sites and nice averaging leads to lower Flicker Noise.
In Pseudomorphic materials it is a function of critical thickness. In quantum well devices like pHEMT it is dependent on material lattice constants.
Flicker Noise Spectral Density

## Slide 150: Burst Noise
Source of Burst Noise is the alloy (heavy metal) contamination. Usually gold doped devices show high level of burst noise. Heavy metal ions are capture sites and time constants are large. This causes pulses of current at much lower frequencies in audio range (few KHz). The period and width of pulses is random resulting in following spectral content-
where is process dependent parameter
c can vary between 0.5 to 2
t
Noise Current Amplitude
Burst Noise Amplitude Pulses
f
Burst Noise Spectral Density

## Slide 151: LNA Specifications in context of Receiver
LNA Specifications | Receiver Performance
LNA Gain | SFDR, Sensitivity
LNA Bandwidth and Roll-off | Image and ½ IF rejection, Sensitivity
LNA Noise Figure | Sensitivity, SFDR
Insertion Loss of Input Match | Sensitivity
LNA Linearity (SOI, TOI, Pin-1dB, AM-AM, AM-PM) | Selectivity, Inter-channel interference, SFDR
LNA Reverse Isolation | Self Demodulation of Carrier leading to DC Wandering in Direct Conversion Transceivers
LNA Ruggedness | Receiver Ruggedness
Target LNA Specifications
Characteristics | Specifications
Frequency Band | 8.5 to 11 GHz
Gain | 18 to 20 dB
I/O Return Loss | < -10 dB
Noise Figure | < 2.1 dB
Quiescent Current | < 65 mA (Vdd=15 V, 975 mW)
Pin @ -1 dB | -5 dBm
Input TOI | 10 dBm
Input SOI | 20 dBm
Assuming 24 dB isolation of Switch and peak output of PA to be 42 dBm. LNA should survive peak input power of 18 dBm. LNA will be switched off when PA is on

## Slide 152: Exercise 15: LNA design in UMS GH25 Process
In this exercise we will learn to design and layout a two stage LNA in UMS GH25 Process

## Slide 153: Two Stage LNA
1
Use GH25LNF Model for the device. Bias is established by current density and size. Size the device and fix current density for desired quiescent current. Transistor gate bias is to merely provide AC ground and its value has to be adjusted to establish the current density using the GH25NHF device model with same device size.

## Slide 154: Single and Two Stage Design
2
Use the device with the following size and current density. Use Source Degeneration and RC feedback to stabilize the device.
3
Use only capacitors and microstrip lines to simultaneously match input and output for best Return Loss and Noise Figure
4
Follow the same procedure to design the second stage The primary goal from second stage is the Gain and not the Noise Figure with least quiescent current. Cascade both the stages. Remove large series capacitors in case they are not required.

## Slide 155: Small Signal Response of LNA

## Slide 156: First Stage Stability Circles
Load and Source Stability Circles completely enclose the Smit Chart or are completely outside the Smith Chart
Matched Stage is absolutely Stable

## Slide 157: Second Stage Stability Circles
Load and Source Stability Circles completely enclose the Smit Chart or are completely outside the Smith Chart
Matched Stage is absolutely Stable

## Slide 158: Two Stage Stability

## Slide 159: Implementing Input Match
Circuit
EM

## Slide 160: Implementing Input Match
Circuit
EM

## Slide 161: Implementing Input Match
Circuit
EM

## Slide 162: Implementing Input Match

## Slide 163: EM Simulated Input Match
Circuit
EM

## Slide 164: Testing with Input Match

## Slide 165: Inter-stage Simplification
In the design process each stage was matched to 50 Ohm and the stages were simply cascaded
Load Match
50Ω
Source Match

## Slide 166: Inter-stage Simplification
From Previous Slide

## Slide 167: Inter-stage Simplification
From Previous Slide

## Slide 168: Inter-stage Simplification
From Previous Slide

## Slide 169: Performance with simplified Inter-stage

## Slide 170: Source Degeneration on Stage 1
Circuit
EM

## Slide 171: Performance with Source Degeneration

## Slide 172: Inter-stage Implementation
Circuit
EM

## Slide 173: Inter-stage Implementation
Circuit
EM

## Slide 174: Inter-stage Implementation
Circuit
EM

## Slide 175: Inter-Stage Implementation
Circuit
EM

## Slide 176: Inter-stage Implementation
Circuit
EM

## Slide 177: Inter-stage Implementation
Circuit
EM

## Slide 178: LNA with Inter-stage EM Model

## Slide 179: Response with Inter-stage EM Model

## Slide 180: Source Degeneration of Second Stage

## Slide 181: Performance with Source Degeneration

## Slide 182: Load Match Implementation
Circuit
EM

## Slide 183: Load Match Implementation
Circuit
EM

## Slide 184: Load Match Implementation
Circuit
EM

## Slide 185: Load Match Implementation
Circuit
EM

## Slide 186: Load Match Implementation
Circuit
EM

## Slide 187: LNA with all Matching

## Slide 188: LTCC Module

## Slide 189: LNA Performance with LTCC Package
Conclusion
We will loose 0.4 to 0.6 dB in Noise Figure due to mismatch on package pins and losses in bond wires. Gain Flatness will also be affected.
3Ω mismatch in 50Ω system roughly corresponds to 1 dB loss in gain.

## Slide 190: LNA Layout (DRC clean)
Scope for Size Reduction

## Slide 191: Power Amplifier Fundamentals
Design considerations for Communication System

## Slide 192: Role of Power Amplifier in Communication System
Ideally, Power Amplifier amplifies the output of a Transceiver to Power Level that would be enough for signal to get through the medium to a receiver where it can be faithfully demodulated. Faithfully Demodulated refers to satisfying a certain Bit-Error-Rate (BER) upon demodulation.
Tolerable non-Ideal characteristics of a PA depend upon its application. These non-ideal characteristics have to be optimized by a designer.
LNA
VCO
Mixer
BPF
Antenna
Baseband
PA
VCO
Mixer
BPF
Antenna
Baseband
Path Loss
Attenuation
Fading
Noise
Receiver
Transmitter
Power Amplifier (PA) amplifies signal power to compensate for signal degradation in channel so as to maintain signal integrity and minimum S/N Ratio required at the Receiver

## Slide 193: PA in FDD Vs TDD System
PA
LNA
Radio Front End (RFE) shares antenna between Transmitter and Receiver.
PA
LNA
In Time Division Duplex (TDD) Transmit & Receive takes place in Different Time Slots
In Frequency Division Duplex (FDD) Transmit & Receive takes place in Different Frequency Bands
PA is operated in pulsed mode in TDD Systems while in FDD Systems it is operated continuously

## Slide 194: PA Topologies at a glance
Class-A
Class-AB
Class-B
Class-C
Power Amplifier
Switching Amplifier
Non-Switching Amplifier
Mixed Mode Amplifier
Class D
Class E
Class F
Class A
Class B
Class AB
Class C
 | Class-A | Class-AB | Class-B Push-pull | Class-C
Conduction Angle | 360⁰ | >180⁰ <360⁰ | 360⁰ | <180⁰
Device Utilization Factor | 0.125 | 0.125 | 0.125 | 0.0981 @ 120⁰
Ideal Maximum Efficiency | 25% | <78% | 78.4% | 89.6% @ 120⁰
Application | Audio | Data & Voice Communication | Audio | Data & Voice Communication

## Slide 195: PA Specifications and Constraints
PA Specifications
Gain
Power Gain
Available Gain
Transducer Gain
Efficiency
Drain Efficiency
Power Added Eff.
Conversion Eff.
Return Loss
Linearity
Adjacent Channel Power Ratio
Error Vector Magnitude
Third Order Intercept
Stability
Turn on time/Receive Band Noise
Ruggedness
Yield
MTTF, MTBF
Quiescent Current
Constraints
Size
Temperature Range
Supply Voltage Range
Component Count

## Slide 196: Gain
PA
Let us assume ideal circulators at the input and output of PA to distinguish between incident, transmitted and reflected power at Input and Output of PA.
Power Gain
Power Gain absorbs both output and input mismatch losses. Power Gain is given by
Available Gain
Available Gain does not absorb any mismatch losses and is true measure of gain of a PA.
Transducer Gain
Transduce Gain absorbs mismatch at the output of PA and not at the input of PA.

## Slide 197: S-Parameters and Return Losses
Forward Gain
Reverse Gain
Return Loss
Special Case
Special Case

## Slide 198: Efficiency
Power Amplifier delivers high power to antenna (may be a switch or a circulator in between). PA drains maximum DC power and hence is critical component from viewpoint of efficiency. Power drawn from DC Supply not delivered to output is dissipated as heat. Hence high efficiency is also desirable for cooler operation of handset. Efficiency can be defined in three ways
Drain/Collector Efficiency
Power Added Efficiency
Conversion Efficiency

## Slide 199: Single Tone Characteristics of PA
Power Input (dBm)
Gain (dB)
Output Power (dBm)
Linear Region
Nonlinear Region
Saturated Region
PAE (%)
Gain
Output Power
PAE
Linear Region
Non-Linear Region
Linear
Non-Linear
Here Pin is input power and can be single tone, multi-tone or Fourier expansion of any periodic waveform

## Slide 200: Two Tone
Input is applied to PA operation in non-linear region
Linear Component of Output Power
Let us assume two tones with frequencies and such that and =∆𝑓 tends to zero.
Principle of Superposition can be applied to each tone giving Linear Components of output power as Gain times the two tones.

## Slide 201: Second Order Mixing
Power Input (dBm)
ISOI
OSOI
Output Power (dBm)
Second Order Mix Components vs. Input Power
In non-linear region second order mix components are offered twice the gain compared to gain offered to tones in linear region i.e. they grow faster with increased input power compared to two tones.
Second Order Mix Spectral Components

## Slide 202: Third Order Mixing
Third Order Mix Spectral Components
Third Order Mix Components vs. Input Power
ISOI
OSOI
Output Power (dBm)
Power Input (dBm)
ITOI
OTOI
Figure shows that Odd-Order Mixing results in spectral components adjacent to the main channel. PA Non-linearity thus results in Spectral Regrowth

## Slide 203: Adjacent Channel Power Ratio (ACPR)
In case of Band Limited Signal around a tone, odd order mixing results in adjacent channel interference
Adjacent Channel Power Ratio
Main Channel
Adjacent Channel
Adjacent Channel
Adjacent Bands due to Odd Order Mixing for Modulated (Band-Limited) Input
Note that adjacent channel power expressed in dB below Main Channel Power (dBc) is referred to as Adjacent Channel Power Ratio (ACPR).

## Slide 204: AM-AM Conversion
Time
Amplitude
Pure Tone
AM-AM Distorted Tone
Phasor Representation of Tone
In-Modulation Comp.
In-Modulation Comp.
Pure Tone
AM-AM Distorted Tone
Mix Components that are generated through mixing of tone with itself and its harmonics may result in components at same frequency as the tone. In case they are in sync with phase of the tone, these in-modulation components result in Amplitude Modulation. This phenomenon is referred to as AM to AM Conversion.

## Slide 205: AM-PM Conversion
AM to PM Conversion
In-Modulation Comp.
Phasor Representation of Tone
In-Modulation Comp.
Pure Tone
AM-PM Conversion
Another scenario is when In-modulation component in previous demonstration appear with phase offset in respect to Tone. In such situation the resultant Phasor Representation shows Phase Modulation along with AM-AM Conversion. This is referred to as AM-PM Conversion.

## Slide 206: Error Vector Magnitude
Effect of I & Q Imbalance
Effect of PA Compression
Compressed Constellation
Original Constellation
Symbols Not Affected by Compression
Symbols Worst Affected by Compression
Error Vector Magnitude
Demodulated Constellation
Original Constellation
Output Power (dBm)
BER
%EVM
Acceptable BER
Acceptable %EVM
BER & %EVM vs. Output Power
Average EVM over all symbols expressed in dB is called Average Relative Constellation Error (RCE)

## Slide 207: Exercise 16: Power Amplifier Design
PA Design in UMS GaN Process

## Slide 208: Typical Power Densities in UMS Processes
UMS GaN GH25
4 Watt / mm of Gate Width
Typical Supply Voltage 12 V< <30 V
Typical Gate Bias -3.2 V
= 30 GHz
UMS GaAs PPH25
0.7 Watt / mm of Gate Width
Typical Supply Voltage 6 V< <12 V
Typical Gate Bias -0.7 V
= 45 GHz
Issues
Gain has soft compression
Inductors have high Q but Bandwidth is difficult to achieve
Issues
Large Size
Complicated Power Combining

## Slide 209: Power Amplifier Specifications
Specifications | min | typ | max
 | 25 V | 28 V | 30 V
 | 0.8 A | 1 A | 1.2 A
Gain | 23 dB | 25 dB | 27 dB
 | 41 dBm | 42 dBm | 42.5 dBm
Return Loss | -15 dB | -12 dB | -9 dB
Compression | -3 dB | -4 dB | -5 dB
PAE | 33% | 35% | 38%
Specifications | min | typ | max
 | 25 V | 28 V | 30 V
 | 0.8 A | 1 A | 1.2 A
Gain | 23 dB | 25 dB | 27 dB
 | 41 dBm | 42 dBm | 42.5 dBm
Return Loss | -15 dB | -12 dB | -9 dB
Compression | -3 dB | -4 dB | -5 dB
PAE | 33% | 35% | 38%

## Slide 210: Balanced Power Stage Design
1
Put together the balanced power stage for PA as shown.

## Slide 211: ADS Bench for Tuning
2
Create the PA Test Bench as shown in figure

## Slide 212: HB Simulation Results from Power Stage
8.5 GHz to 10.5 GHz
3
Use Tune to achieve the desired specifications. Alternatively you can use optimization to fine tune the performance.

## Slide 213: Driver Stage
4
Follow the procedure, discussed previously for Power Stage, to implement Driver Stage and Pre-driver stage.

## Slide 214: ADS Bench for Tuning Driver Stage

## Slide 215: HB Simulation Results from Driver Stage
8.5 GHz to 10.5 GHz

## Slide 216: Complete Three Stage

## Slide 217: Circuit Simulation Results
Variation across frequency should not be source of concern. Experience shows that this variation is not noticeable in EM Co-Simulation.

## Slide 218: Load Match Implementation
Package Line Equivalent

## Slide 219: Load Match Implementation

## Slide 220: Load Implementation

## Slide 221: Complete Power Stage for EM Co-Sim.
Circuit
EM Co-Sim.

## Slide 222: Complete Class E Driver Stage
Circuit
EM Co-Sim.

## Slide 223: Complete Pre-Driver
Circuit
EM Co-Sim.

## Slide 224: EM-Circuit Co-simulation of PA

## Slide 225: Across Frequency Performance

## Slide 226: Across Power Performance
Stats
Small Signal Gain 32 dB
2 dB compressed at 10.5 Watt
5 dB compresses at 15 Watt
Worse case return loss -7 dB
PAE at -2dB Compression is 34.3 %
PAE at -5dB Compression is 35.6%

## Slide 227: PA Layout as EM Co-simulated

## Slide 228: Phase Shifter Fundamentals
Low Pass/ High Pass and Band Pass Networks

## Slide 229: Topology Overview
Difference in delay in two paths through an element gives the desired phase shift.
Both elements have same characteristics across frequency but one has positive delay while the other one has negative delay resulting in twice the delay contributed by switching one element. The variation across frequency is cancelled resulting in broadband nature of delay.
Each delay element has attenuation that has to be compensated by a gain stage following the phase shifter.
Phase Error on each element can be absolute or relative in percentage. The over all phase error is RMS value of individual contributions.

## Slide 230: High Pass/ Low Pass Networks
High Pass T
Low Pass π
For less number of Inductors
HP
LP
Many combinations are possible to realize a Bandwidth as high as 70% with rms PE < 5%

## Slide 231: Exercise 17: Digital Phase Shifter Design
Digital Phase Shifter in GaN Process

## Slide 232: Single Pole Double Throw Switch

## Slide 233: Response of SPDT Switch

## Slide 234: Delay Elements
Realizing HP/LP Delay elements is easy using network theory rather than formulas

## Slide 235: 180⁰ Delay using HP & LP
PE

## Slide 236: 90⁰ Delay using HP & LP

## Slide 237: 45⁰ Delay using HP & LP

## Slide 238: 22.5⁰ Delay using HP & BP

## Slide 239: 11.25⁰ Delay using HP & BP

## Slide 240: 5.625⁰ Delay using HP & BP

## Slide 241: 6-Bit Phase Shifter

## Slide 242: Simulating 6-bit Phase Shifter

## Slide 243: Questions & Answers
Please let us know how we can work further!